## Slide 1
RVfpga
The Complete Course in Understanding Computer Architecture

## Slide 2: Acknowledgements
Sponsors and Supporters
AUTHORS
Prof. Sarah Harris
Prof. Daniel Chaver
Zubair Kakakhel
M. Hamza Liaqat
ADVISER
Prof. David Patterson
CONTRIBUTORS
Robert Owen
Olof Kindgren
Prof. Luis Piñuel
Ivan Kravets
Valerii Koval
Ted Marena
Prof. Roy Kravitz
ASSOCIATES
Prof. José Ignacio Gómez
Prof. Christian Tenllado
Prof. Daniel León
Prof. Katzalin Olcoz
Prof. Alberto del Barrio
Prof. Fernando Castro
Prof. Manuel Prieto
Prof. Francisco Tirado
Prof. Román Hermida
Prof Ataur Patwary
Cathal McCabe
Dan Hugo
Braden Harwood
Prof. David Burnett
Gage Elerding
Prof. Brian Cruickshank
Deepen Parmar
Thong Doan
Oliver Rew
Niko Nikolay
Guanyang He

## Slide 3: Introduction
RISC-V FPGA (RVfpga) is a teaching package that provides a set of instructions, tools, and labs that show how to:
  Target a commercial RISC-V system-on-chip (SoC) to an FPGA
  Program the RISC-V SoC
  Add more functionality to the RISC-V SoC
  Analyze and modify the RISC-V core and memory hierarchy
The package is being developed by Imagination Technologies and its academic and industry partners.
The RVfpga System is built around Chips Alliance’s SweRVolf SoC, which is based on Western Digital’s RISC-V SweRV EH1 core.

## Slide 4: RVfpga Overview
The RVfpga Package provides:
  a comprehensive, freely distributed, complete RISC-V course
  a hands-on and easily accessible way to learn about RISC-V processors and the RISC-V ecosystem
  a RISC-V system targeted to low-cost FPGAs, which are readily available at many universities and companies.
After completing the RVfpga Course, users will walk away with a working RISC-V processor, SoC, and ecosystem that they understand and know how to use and modify.

## Slide 5: RVfpga Course Contents

## Slide 6: RVfpga Contents
Getting Started Guide
  Quick Start Guide
  Overview of RISC-V Architecture and RVfpga
  Installing Tools (VSCode, PlatformIO, Vivado, Verilator, and Whisper)
  Running the RVfpga System in Hardware and Simulation
Labs
  1-10: Building the RVfpga System in Vivado, Programming and Extending the system by adding peripherals (released Nov 2020)
  11-20: Analyzing and modifying RVfpga’s RISC-V core and memory system (to be released Q4 2021)

## Slide 7: RVfpga Course
2-4 Semester Course
  Undergraduate (Labs 1-10)
  Master’s/upper division (Labs 11-20)
Expected Prior Knowledge
  Fundamental understanding of digital design, high-level programming (preferably C), instruction set architecture and assembly programming, processor microarchitecture, memory systems (this material is covered in Digital Design and Computer Architecture: RISC-V Edition, Harris & Harris, © Elsevier, expected publication: summer 2021)
  These topics will be expanded on and solidified with hands-on learning throughout the RVfpga course

## Slide 8: How to Get RVfpga
Register for Imagination University Programme (IUP) – for teachers, researchers, and students worldwide:
https://university.imgtec.com
  Receive updates and notifications of release
  Request & download materials
  Support Forums: PowerVR, RVfpga, & AI Forums; IUP Forum for curriculum/teaching discussions
Social Media:
  Robert Owen, IUP Director: @UniPgm
  Imagination Technologies: @ImaginationTech
  WeChat & Weibo: ImaginationTech
Scan QR Code for IUP website
Imagination University Programme Website

## Slide 9: RVfpga Required Software and Hardware
SOFTWARE
Xilinx Vivado 2019.2 WebPACK
PlatformIO – an extension of Microsoft’s Visual Studio Code – with Chips Alliance platform, which includes: RISC-V Toolchain, OpenOCD, Verilator HDL Simulator, WD Whisper instruction set simulator (ISS)
HARDWARE*
Digilent’s Nexys A7 / Nexys 4 DDR FPGA Board
RISC-V CORE & SOC
Core: Western Digital’s SweRV EH1
SoC: Chips Alliance’s SweRVolf
All are free except for the FPGA board, which costs $265 (academic price: $199)
*All labs can be completed in simulation only; so this hardware is recommended but not required.

## Slide 10: Supported Platforms
Operating Systems
  Ubuntu 18.04 (although later versions likely also work)
  Windows 10
  macOS

## Slide 11: RVfpga Software Tools
Xilinx’s Vivado IDE
  View RVfpga source files (Verilog / SystemVerilog) and hierarchy
  Create bitfile (FPGA configuration file) for RVfpga targeted to Nexys A7 board
PlatformIO – an extension of Visual Studio Code (VSCode)
  Download the RVfpga System onto the Nexys A7 board
  Compile, download, run, and debug C and assembly programs on the RVfpga System
Verilator – an HDL (hardware description language) simulator
  Simulate the RVfpga System at HDL (low) level to analyze its internal signals

## Slide 12: Nexys A7-100T FPGA Board
figure of board from https://reference.digilentinc.com/
Contains Artix-7 field programmable gate array (FPGA)
Includes peripherals (i.e., LEDs, switches, pushbuttons, 7-segment displays, accelerometer, temperature sensor, microphone, etc.)
Available for purchase at digilentinc.com and other vendors

## Slide 13: RISC-V Cores and SoCs

## Slide 14: RVfpga Hierarchy

## Slide 15: RVfpga Hierarchy
Name | Description
SweRV EH1 Core | Open-source commercial RISC-V core developed be Western Digital (https://github.com/chipsalliance/Cores-SweRV).
SweRV EH1 Core Complex | SweRV EH1 core with added memory (ICCM, DCCM, and instruction cache), programmable interrupt controller (PIC), bus interfaces, and debug unit (https://github.com/chipsalliance/Cores-SweRV).
SweRVolfX (Extended SweRVolf) | The System on Chip that we use in the RVfpga course. It is an extension of SweRVolf. SweRVolf (https://github.com/chipsalliance/Cores-SweRVolf): An open-source SoC built around the SweRV EH1 Core Complex. It adds a boot ROM, UART interface, system controller, interconnect (AXI Interconnect, Wishbone Interconnect, and AXI-to-Wishbone bridge), and an SPI controller. SweRVolfX: It adds 4 new peripherals to SweRVolf: a GPIO, a PTC, an additional SPI and a controller for the 8 digit 7-Segment Displays.
RVfpgaNexys | The SweRVolfX SoC targeted to the Nexys A7 board and its peripherals. It adds a DDR2 interface, CDC (clock domain crossing) unit, BSCAN logic (for the JTAG interface), and clock generator. RVfpgaNexys is the same as SweRVolf Nexys (https://github.com/chipsalliance/Cores-SweRVolf), except that the latter is based on SweRVolf.
RVfpgaSim | The SweRVolfX SoC with a testbench wrapper and AXI memory intended for simulation. RVfpgaSim is the same as SweRVolf sim, (https://github.com/chipsalliance/Cores-SweRVolf), except that the latter is based on SweRVolf.

## Slide 16: SweRV EH1 Core and SweRV EH1 Core Complex
Figure from https://github.com/chipsalliance/Cores-SweRV/blob/master/docs/RISC-V_SweRV_EH1_PRM.pdf
Open-source core from Western Digital
32-bit (RV32ICM) superscalar core, with dual-issue 9-stage pipeline
Separate instruction and data memories (ICCM and DCCM) tightly coupled to the core
4-way set-associative I$ with parity or ECC protection
Programmable Interrupt Controller
Core Debug Unit compliant with the RISC-V Debug specification
System Bus: AXI4 or AHB-Lite

## Slide 17: SweRVolfX SoC
Open-source system-on-chip (SoC) from Chips Alliance
SweRVolf uses the SweRV EH1 Core. SweRVolf includes a Boot ROM, UART, and a System Controller and an SPI controller (SPI1)
SweRVolfX extends SweRVolf with another SPI controller (SPI2), a GPIO (General Purpose Input/Output), 8-digit 7-Segment Displays and a PTC (shown in red).
SweRV EH1 Core uses an AXI bus and peripherals use a Wishbone bus, so the SoC also has an AXI to Wishbone Bridge
System | Address
Boot ROM | 0x80000000 - 0x80000FFF
System Controller | 0x80001000 - 0x8000103F
SPI1 | 0x80001040 - 0x8000107F
SPI2 | 0x80001100 - 0x8000113F
Timer | 0x80001200 - 0x8000123F
GPIO | 0x80001400 - 0x8000143F
UART | 0x80002000 - 0x80002FFF
SweRVolfX Memory Map

## Slide 18: RVfpgaNexys
RVfpgaNexys: SweRVolfX SoC targeted to Nexys A7 FPGA board with added peripherals:
  Core & System:
    SweRVolfX SoC
    Lite DRAM controller
    Clock Generator, Clock Domain
    and BSCAN logic for the JTAG port
  Peripherals used on Nexys A7 FPGA board:
    DDR2 memory
    UART via USB connection
    SPI Flash memory
    16 LEDs and 16 switches
    SPI Accelerometer
    8-digit 7-segment displays

## Slide 19: RVfpgaSim
The SweRVolfX SoC can also include a Verilog wrapper to enable simulation.
RVfpgaSim is the SweRVolfX SoC wrapped in a testbench to be used by HDL simulators.

## Slide 20: Rvfpga System Extensions
The Rvfpga System is further extended in Labs 6-10:
  Another GPIO controller to interface with the on-board Nexys A7 pushbuttons
  Modification of the 7-segment displays controller
  New timer modules for using the on-board tri-color LEDs
  New external interrupt sources

## Slide 21: RVfpga Labs Overview

## Slide 22: RVfpga Labs
Labs 1-10 (released Nov 2020)
Vivado Project and Programming
I/O Systems
Labs 11-20 (to be released Q4 2021)
RISC-V Core
RISC-V Memory Systems
All labs include exercises for using and/or modifying the RVfpga System to increase understanding through hands-on design.

## Slide 23: RVfpga Labs 1-10
Show how to view the RVfpga System source code (Verilog/SV) and target it to an FPGA (Lab 1), write C and assembly programs (Labs 2-5), and modify RVfpgaNexys/RVfpgaSim to add peripherals (Labs 6-10).
Lab 0: Overview of RVfpga Labs
Lab 1: Creating a Vivado Project
Lab 2: C Programming
Lab 3: RISC-V Assembly Language
Lab 4: Function Calls
Lab 5: Image Processing: C & Assembly
Lab 6: Introduction to I/O
Lab 7: 7-Segment Displays
Lab 8: Timers
Lab 9: Interrupt-driven I/O
Lab 10: Serial Buses
Programming
I/O Systems

## Slide 24: RVfpga Labs 1-5: Vivado Project & Programming
Lab 1: Creating a Vivado Project: Build a Vivado project to target RVfpgaNexys to an FPGA board and simulate RVfpgaSim in Verilator
Lab 2: C Programming: Write a C program in PlatformIO, and run / debug it on RVfpgaNexys/RVfpgaSim/Whisper. Also introduce Western Digital’s Board Support and Platform Support Packages (BSP and PSP) for supporting operations such as printing to the terminal.
Lab 3: RISC-V Assembly Language: Write a RISC-V assembly program in PlatformIO and run /debug it on RVfpgaNexys/RVfpgaSim/Whisper
Lab 4: Function Calls: Introduction to function calls, C libraries, and the RISC-V calling convention
Lab 5: Image Processing: C & Assembly: Embed assembly code with C code

## Slide 25: RVfpga Labs 6-10: I/O & Peripherals
Lab 6: Introduction to I/O: Introduction to memory-mapped I/O and RVfpga System’s open-source GPIO module
Lab 7: 7-Segment Displays: Build a 7-segment display decoder and integrate it into the RVfpga System
Lab 8: Timers: Understand and use Timers and a Timer controller
Lab 9: Interrupt-driven I/O: Introduction to Rvfpga System interrupt support and use of interrupt-driven I/O
Lab 10: Serial Buses: Introduction to serial interfaces (SPI, I2C, UART). Use on board accelerometer that uses an SPI interface

## Slide 26: RVfpga Labs 11-15: The RISC-V Core
To be released in Q4 2021
Understanding the core structure
Understanding instruction flow through the pipeline (Arithmetic/Logic, Memory, Jumps, and Branches)
Understanding hazards and how to deal with them
Implementing new instructions and executing them on the FPGA board
Understanding and modifying the branch predictor
Understanding superscalar processing

## Slide 27: RVfpga Labs 16-20: RISC-V Memory Systems
To be released in Q4 2021
Understanding the operation of the memory hierarchy including cache hits and misses
Modifying the cache: implementing different cache sizes, configurations, and management policies
Understanding the cache controller
Understanding the memories: ICCM (instruction closely coupled memory) and DCCM (data closely coupled memory)

## Slide 28: RVfpga Timeline
Target Audience
  Undergraduates in electrical engineering, computer science, or computer engineering
  Academics & Industry professionals interested in learning the RISC-V architecture
Imagination University Programme (IUP) Track Record: Developed MIPSfpga Program:
  Launched in April 2015
  Engaged 800 universities
  Winner: Elektra Best Educational Support Award, Europe 2015
RVfpga Availability | 
November 2020 | RVfpga Getting Started Guide RVfpga Labs 1-10
Q4 2021 | RVfpga Labs 11-20
June 2021 | Masters-level SoC Design Course
Languages | English & Chinese (Spanish & Japanese to follow)
Textbook | Digital Design & Computer Architecture: RISC-V Edition 2021 by Sarah Harris and David Harris

## Slide 29: RVfpga Quick Start Guide

## Slide 30: Quick Start Guide Overview
Install VSCode & PlatformIO
Run Example Program on RVfpgaNexys

## Slide 31: Install PlatformIO & VSCode
Install VSCode
  https://code.visualstudio.com/Download
  For Ubuntu and macOS, install Python (this step is not required for Windows)
Install PlatformIO extension within VSCode
Install Nexys A7 Board drivers (see RVfpga Getting Started Guide instructions)

## Slide 32: Download RVfpgaNexys onto Board and Run Program
In PlatformIO:
  Open example program that writes value of switches to LEDs. Program is in: [RVfpgaPath]\RVfpga\examples\LedsSwitches_C-Lang
  Update directory location of RVfpgaNexys bitfile in PlatformIO initialization file (platformio.ini) – i.e., add this line to platformio.ini: board_build.bitstream_file = [RVfpgaPath]/RVfpga/src/rvfpga.bit
  Download RVfpgaNexys onto Nexys A7 Board (Project Tasks → env:swervolf_nexys → Platform → Upload Bitstream)
  Compile, download, and run program on RVfpgaNexys by pressing the Run/Debug button:
[RVfpgaPath] is the location of the RVfpga folder on your machine. This folder was provided with the RVfpga package from the Imagination University Programme.

## Slide 33: RVfpga Labs Descriptions

## Slide 34: Lab 1: Vivado Project

## Slide 35: RVfpga Lab 1: RVfpga Vivado Project
Vivado is a Xilinx tool for viewing, modifying, and synthesizing the source (Verilog) code for the RVfpga System.
RVfpga System’s source code is in:
[RVfpgaPath]/RVfpga/src
Create a Vivado project that contains RVfpga System’s source code. Synthesize RVfpgaNexys targeted to Nexys A7 board and create a bitfile (also called bitstream file) that contains information to configure the FPGA as RVfpgaNexys.
You may also use Verilator, an HDL simulator, to simulate RVfpga System’s source code and examine internal signals (see the RVfpga Getting Started Guide for instructions on how to use Verilator).
Vivado and Verilator will be used extensively in RVfpga Labs 6-10 for modifying and simulating the RVfpga System.

## Slide 36: Lab 2: C Programming

## Slide 37: RVfpga Lab 2: C Programming
Create PlatformIO project
Add example C program to project
Download RVfpgaNexys to Nexys A7 board
Download C program onto RVfpgaNexys and run/debug program
Complete some or all of exercises at end of lab
Remember that you can also simulate the program in Verilator (using RVfpgaSim) or Whisper.

## Slide 38: RVfpga Lab 2: Example C Program
// memory-mapped I/O addresses
#define GPIO_SWs 0x80001400
#define GPIO_LEDs 0x80001404
#define GPIO_INOUT 0x80001408
#define READ_GPIO(dir) (*(volatile unsigned *)dir)
#define WRITE_GPIO(dir, value) { (*(volatile unsigned *)dir) = (value); }
int main ( void )
{
int En_Value=0xFFFF, switches_value;
WRITE_GPIO(GPIO_INOUT, En_Value);
while (1) {
switches_value = READ_GPIO(GPIO_SWs); // read value on switches
switches_value = switches_value >> 16; // shift into lower 16 bits
WRITE_GPIO(GPIO_LEDs, switches_value); // display switch value on LEDs
}
return(0);
}
This program writes the value of the switches to the LEDs.

## Slide 39: RVfpga Lab 2: Memory-Mapped I/O Addresses
Device | Memory-Mapped I/O Address
Switches (16 on Nexys A7 board) | 0x80001400 (upper 16 bits)
LEDs (16 on Nexys A7 board) | 0x80001404 (lower 16 bits)
Input/Output of GPIO (1 = output, 0 = input) | 0x80001408

## Slide 40: RVfpga Lab 2: Western Digital’s BSP & PSP
Western Digital provides:
  PSP: processor support package
  BSP: board support package
These provide common functions for a given processor (SweRV EH1 core) and board (Nexys A7 FPGA board).
  Example: printfNexys (like printf function in C)

## Slide 41: RVfpga Lab 2: Using UART to Print to Terminal
#if defined(D_NEXYS_A7)
#include <bsp_printf.h>
#include <bsp_mem_map.h>
#include <bsp_version.h>
#else
PRE_COMPILED_MSG("no platform was defined")
#endif
#include <psp_api.h>
#define DELAY 10000000
int main(void) {
int i, j = 0;
// Initialize UART
uartInit();
while (1) {
printfNexys("Hello RVfpga users! Iteration: %d\n", j);
for (i=0; i < DELAY; i++) ; // delay between printf's
j++;
}
}
Add this line to platform.ini file:
monitor_speed = 115200
After program starts running, open PlatformIO terminal by pressing this button in the bottom of the window:

## Slide 42: Lab 3: RISC-V Assembly

## Slide 43: RVfpga Lab 3: RISC-V Assembly
RISC-V Assembly Language Overview
Create PlatformIO project
Add example RISC-V assembly program to project
Download RVfpgaNexys to Nexys A7 board
Download RISC-V assembly program onto RVfpga and run/debug program
Complete some or all of exercises at end of lab
Remember that you can also simulate the program in Verilator (using RVfpgaSim) or Whisper.

## Slide 44: RVfpga Lab 3: RISC-V Assembly Instructions
Common RISC-V Assembly Instructions/Pseudoinstructions
RISC-V Assembly | Description | Operation | 
add s0, s1, s2 | Add | s0 = s1 + s2 | 
sub s0, s1, s2 | Subtract | s0 = s1 - s2 | 
addi t3, t1, -10 | Add immediate | t3 = t1 – 10 | 
mul t0, t2, t3 | 32-bit multiply | t0 = t2 * t3 | 
div s9, t5, t6 | Division | t9 = t5 / t6 | 
rem s4, s1, s2 | Remainder | s4 = s1 % s2 | 
and t0, t1, t2 | Bit-wise AND | t0 = t1 & t2 | 
or t0, t1, t5 | Bit-wise OR | t0 = t1 ¦ t5 | 
xor s3, s4, s5 | Bit-wise XOR | s3 = s4 ^ s5 | 
andi t1, t2, 0xFFB | Bit-wise AND immediate | t1 = t2 & 0xFFFFFFFB | 
ori t0, t1, 0x2C | Bit-wise OR immediate | t0 = t1 ¦ 0x2C | 
xori s3, s4, 0xABC | Bit-wise XOR immediate | s3 = s4 ^ 0xFFFFFABC | 
sll t0, t1, t2 | Shift left logical | t0 = t1 << t2 | 
srl t0, t1, t5 | Shift right logical | t0 = t1 >> t5 | 
sra s3, s4, s5 | Shift right arithmetic | s3 = s4 >>> s5 | 
slli t1, t2, 30 | Shift left logical immediate | t1 = t2 << 30 | 
srli t0, t1, 5 | Shift right logical immediate | t0 = t1 >> 5 | 
srai s3, s4, 31 | Shift right arithmetic immediate | s3 = s4 >>> 31 | 

## Slide 45: RVfpga Lab 3: RISC-V Assembly Instructions
Common RISC-V Assembly Instructions/Pseudoinstructions (continued)
RISC-V Assembly | Description | Operation | 
lw s7, 0x2C(t1) | Load word | s7 = memory[t1+0x2C] | 
lh s5, 0x5A(s3) | Load half-word | s5 = SignExt(memory[s3+0x5A]15:0) | 
lb s1, -3(t4) | Load byte | s1 = SignExt(memory[t4-3]7:0) | 
sw t2, 0x7C(t1) | Store word | memory[t1+0x7C] = t2 | 
sh t3, 22(s3) | Store half-word | memory[s3+22]15:0 = t315:0 | 
sb t4, 5(s4) | Store byte | memory[s4+5]7:0 = t47:0 | 
beq s1, s2, L1 | Branch if equal | if (s1==s2), PC = L1 | 
bne t3, t4, Loop | Branch if not equal | if (s1!=s2), PC = Loop | 
blt t4, t5, L3 | Branch if less than | if (t4 < t5), PC = L3 | 
bge s8, s9, Done | Branch if not equal | if (s8>=s9), PC = Done | 
li s1, 0xABCDEF12 | Load immediate | s1 = 0xABCDEF12 | 
la s1, A | Load address | s1 = Memory address where variable A is stored | 
nop | Nop | no operation | 
mv s3, s7 | Move | s3 = s7 | 
not t1, t2 | Not (Invert) | t1 = ~t2 | 
neg s1, s3 | Negate | s1 = -s3 | 
j Label | Jump | PC = Label | 
jal L7 | Jump and link | PC = L7; ra = PC + 4 | 
jr s1 | Jump register | PC = s1 | 

## Slide 46: RVfpga Lab 3: RISC-V Registers
32 32-bit registers
Name | Register Number | Use
zero | x0 | Constant value 0
ra | x1 | Return address
sp | x2 | Stack pointer
gp | x3 | Global pointer
tp | x4 | Thread pointer
t0-2 | x5-7 | Temporary variables
s0/fp | x8 | Saved variable / Frame pointer
s1 | x9 | Saved variable
a0-1 | x10-11 | Function arguments / Return values
a2-7 | x12-17 | Function arguments
s2-11 | x18-27 | Saved variables
t3-6 | x28-31 | Temporary variables

## Slide 47: RVfpga Lab 3: Example RISC-V Assembly Program
// memory-mapped I/O addresses
# GPIO_SWs = 0x80001400
# GPIO_LEDs = 0x80001404
# GPIO_INOUT = 0x80001408
.globl main
main:
main:
li t0, 0x80001400 # base address of GPIO memory-mapped registers
li t1, 0xFFFF # set direction of GPIOs
# upper half = switches (inputs) (=0)
# lower half = outputs (LEDs) (=1)
sw t1, 8(t0) # GPIO_INOUT = 0xFFFF
repeat:
lw t1, 0(t0) # read switches: t1 = GPIO_SWs
srli t1, t1, 16 # shift val to the right by 16 bits
sw t1, 4(t0) # write value to LEDs: GPIO_LEDs = t1
j repeat # repeat loop
This program writes the value of the switches to the LEDs.

## Slide 48: Lab 4: Function Calls

## Slide 49: RVfpga Lab 4: Function Calls
Write C programs with function calls
  Functions are also called procedures
Using C libraries
RISC-V (Procedure) Calling Convention

## Slide 50: RVfpga Lab 4: Example Program with Functions
// memory-mapped I/O addresses
#define GPIO_SWs 0x80001400
#define GPIO_LEDs 0x80001404
#define GPIO_INOUT 0x80001408
#define READ_GPIO(dir) (*(volatile unsigned *)dir)
#define WRITE_GPIO(dir, value) { (*(volatile unsigned *)dir) = (value); }
void IOsetup();
unsigned int getSwitchVal();
void writeValtoLEDs(unsigned int val);
int main ( void ) {
unsigned int switches_val;
IOsetup();
while (1) {
switches_val = getSwitchVal();
writeValtoLEDs(switches_val);
}
return(0);
}

## Slide 51: RVfpga Lab 4: Example Program with Functions
void IOsetup()
{
int En_Value=0xFFFF;
WRITE_GPIO(GPIO_INOUT, En_Value);
}
unsigned int getSwitchVal()
{
unsigned int val;
val = READ_GPIO(GPIO_SWs); // read value on switches
val = val >> 16; // shift into lower 16 bits
return val;
}
void writeValtoLEDs(unsigned int val)
{
WRITE_GPIO(GPIO_LEDs, val); // display val on LEDs
}

## Slide 52: RVfpga Lab 4: C Libraries
Libraries
  Collection of commonly used functions
  Provided so that common functions are readily available (save programming time)
Example C libraries:
  math.h (math library): includes functions such as sqrt (square root), cos (cosine), etc.
  stdio.h (standard I/O library): includes functions for printing values to the screen (printf), reading values from users (scanf), etc.
  stdlib.h (standard library): includes functions for generating random numbers (rand).
  Many others… (google C libraries)

## Slide 53: RVfpga Lab 4: Example Program using C Library
#include <stdlib.h>
...
int main(void) {
unsigned int val;
volatile unsigned int i;
IOsetup();
while (1) {
val = rand() % 65536;
writeValtoLEDs(val);
for (i = 0; i < DELAY; i++)
;
}
return(0);
}
This program writes a random number between 0 and 65535 to the LEDs.

## Slide 54: RVfpga Lab 4: RISC-V Calling Convention
Call a function
  jal function_label
Return from a function
jr ra
Arguments
  placed in registers a0-a7
Return value
  placed in register a0

## Slide 55: RVfpga Lab 4: RISC-V Calling Convention Example
C Code
int main() {
...
  int y = y + func1(1, 2, 3)
  y++;
  ...
  }
  int func1(int a, int b, int c) {
  int sum;
  sum = a + b + c;
  return sum;
  }
RISC-V Assembly
  # y is in s0
  main:
  ...
  addi a0, zero, 1 # put values in argument registers
  addi a1, zero, 2
  addi a2, zero, 3
  jal func1 # call function func1
  add s0, s0, a0 # y = y + return value
  addi s0, s0, 1 # y = y++
  ...
  # sum is in s0
  func1:
  add s0, a0, a1 # sum = a + b
  add s0, s0, a2 # sum = a + b + c
  addi a0, s0, 0 # return value = sum
  jr ra # return

## Slide 56: RVfpga Lab 4: The Stack
Scratch space in memory used to save register values
The stack pointer (sp) holds the address of the top of the stack
The stack grows downward in memory. So, for example, to make space for 4 words (16 bytes) on the stack the following code is used:
addi sp, sp, -16
Two categories of registers:
  Preserved registers: register contents must be preserved across function calls (i.e., contain the same value before and after a function call)
  Non-preserved registers: register contents must not be preserved across function calls (i.e., the register does not need to be the same before and after a function call)
  Saved registers (s0-s11), the return address register (ra), and the stack pointer (sp) are preserved registers. All other registers are not preserved.

## Slide 57: RVfpga Lab 4: Preserved / Nonpreserved Registers
Name | Register Number | Use | Preserved
zero | x0 | Constant value 0 | -
ra | x1 | Return address | Yes
sp | x2 | Stack pointer | Yes
gp | x3 | Global pointer | -
tp | x4 | Thread pointer | -
t0-2 | x5-7 | Temporary variables | No
s0/fp | x8 | Saved variable / Frame pointer | Yes
s1 | x9 | Saved variable | Yes
a0-1 | x10-11 | Function arguments / Return values | No
a2-7 | x12-17 | Function arguments | No
s2-11 | x18-27 | Saved variables | Yes
t3-6 | x28-31 | Temporary variables | No

## Slide 58: RVfpga Lab 4: The Stack – Revised Assembly Code
C Code
int main() {
...
  int y = y + func1(1, 2, 3)
  y++;
  ...
  }
  int func1(int a, int b, int c) {
  int sum;
  sum = a + b + c;
  return sum;
  }
RISC-V Assembly
  # y is in s0
  main: ...
  addi a0, zero, 1 # put values in argument registers
  addi a1, zero, 2
  addi a2, zero, 3
  jal func1 # call function func1
  add s0, s0, a0 # y = y + return value
  addi s0, s0, 1 # y = y++
  ...
  # sum is in s0
  func1:addi sp, sp, -4 # make room on stack
  sw s0, 0(sp) # save s0 on stack
  add s0, a0, a1 # sum = a + b
  add s0, s0, a2 # sum = a + b + c
  addi a0, s0, 0 # return value = sum
  lw s0, 0(sp) # restore s0 from stack
  addi sp, sp, 4 # restore stack pointer
  jr ra # return

## Slide 59: Lab 5: C and Assembly

## Slide 60: RVfpga Lab 5: Combining C and Assembly
Example: Image processing program
Some functions written in C and some in assembly

## Slide 61: RVfpga Lab 5: Image Processing Program
Convert colour image to greyscale

## Slide 62: RVfpga Lab 5: Image Processing Program
Each pixel stored as three 8-bit colours: R = red, G = green, B = blue
Any colour can be created by varying R, G, and B values
To convert image to an 8-bit greyscale (grey), each pixel is transformed as follows:
grey = (306*R + 601*G + 117*B) >> 10
RGB weights add up to 1024 (306 + 601 + 117 = 1024), so to get back to an 8-bit range (0-255), the result is divided by 1024 (i.e., shifted right by 10 bits: >> 10)
For more details about the algorithm, see:
https://www.mathworks.com/help/matlab/ref/rgb2gray.html

## Slide 63: RVfpga Lab 5: Assembly Function
.globl ColourToGrey_Pixel
.text
ColourToGrey_Pixel:
li x28, 306 # a0 = R * 306
mul a0, a0, x28
li x28, 601 # a1 = G * 601
mul a1, a1, x28
li x28, 117 # a2 = B * 117
mul a2, a2, x28
add a0, a0, a1 # grey = a0 + a1 + a2
add a0, a0, a2
srl a0, a0, 10 # grey = grey / 1024
ret # return
.end
grey = (306*R + 601*G + 117*B) >> 10
.globl makes CoulourToGrey_Pixel function visible to all files in project

## Slide 64: RVfpga Lab 5: structs and arrays
typedef struct {
unsigned char R;
unsigned char G;
unsigned char B;
} RGB;
extern unsigned char VanGogh_128x128[]; // 1D array of individual RGB values
RGB ColourImage[N][M]; // 2D array of RGB struct (colour image)
unsigned char GreyImage[N][M]; // 2D array of greyscale image
// VanGogh_128.c
unsigned char VanGogh_128x128[] = { 157, // R (pixel [0][0])
182, // G (pixel [0][0])
161, // B (pixel [0][0])
171, // R (pixel [0][1])
195, // G (pixel [0][1])
173, // B (pixel [0][1])
173, // R (pixel [0][2])
... }

## Slide 65: RVfpga Lab 5: Main Function
int main(void) {
// Create an N x M matrix using the input image
initColourImage(ColourImage);
// Transform Colour Image to Grey Image
ColourToGrey(ColourImage,GreyImage);
...
}
void ColourToGrey(RGB Colour[N][M], unsigned char Grey[N][M]) {
int i,j;
for (i=0; i<N; i++)
for (j=0; j<M; j++)
Grey[i][j] = ColourToGrey_Pixel(Colour[i][j].R, Colour[i][j].G,
Colour[i][j].B);
}

## Slide 66: Lab 6: Intro to I/O

## Slide 67: RVfpga Lab 6: Introduction to I/O
Input/output (I/O) systems – also called peripherals
General-purpose I/O (GPIO)
GPIO controllers

## Slide 68: RVfpga Lab 6: Generic Processor with I/O

## Slide 69: RVfpga Lab 6: Processor with I/O
Peripherals
SweRVolfX peripherals:
  Boot ROM
  System Controller
  SPI1 Flash Memory
  UART
  GPIO LEDs and switches
  Timer
  SPI2 Accelerometer
  7-segment displays (within System Controller: Sys-Con)

## Slide 70: RVfpga Lab 6: General-Purpose I/O (GPIO)
Peripherals
General-purpose I/O:
  Allows processor to read/write pins connected to peripherals (like switches and LEDs)
  Each pin can be configured as an input or output using tri-state
Three memory-mapped registers:
  Read Register: value read from pin
  Write Register: value to write to pin
  Enable Register: 1 = output, 0 = input

## Slide 71: RVfpga Lab 6: Memory-Mapped Registers
Register | Memory-Mapped Address
Read Register | 0x80001400
Write Register | 0x80001404
Enable Register | 0x80001408
Configure bits 15:0 of GPIO as outputs, 31:16 as inputs:
li t0, 0x80001400 # t0 = 0x80001400
li t1, 0xFFFF # 1 = output, 0 = input
sw t1, 8(t0) # [15:0] = outputs, [31:16] = inputs
Reading I/O:
lw t2, 0(t0) # t2 = value of GPIO pins
Writing I/O:
sw t3, 4(t0) # GPIO pins = t3

## Slide 72: RVfpga Lab 6: SweRVolfX GPIO Module
GPIO Module from OpenCores
https://opencores.org/projects/gpio
Allows up to 32 GPIO pins
  All pins can be individually configured as inputs (enable = 0) or outputs (enable = 1)
  Configuration can change throughout program
Register | Memory-Mapped Address
Read Register | 0x80001400
Write Register | 0x80001404
Enable Register | 0x80001408

## Slide 73: RVfpga Lab 6: Memory-Mapped Registers
Mapping LEDs & Switches to GPIO pins:
  LEDS: pins [15:0] (outputs of processor)
  Switches: pins [31:16] (inputs to processor)
Configure GPIO:
  Enable Register = 0x0000FFFF (1 = output, 0 = input)
li t0, 0x80001400
li t1, 0xFFFF
sw t1, 8(t0) # Enable Register = 0xFFFF
Write LEDs:
  Write value in [15:0] to address 0x80001404
  sw t3, 4(t0) # LEDs = [t3]15:0
Read Switches:
  Read switches in bits [31:16] from address 0x80001400
  Shift right by 16 bits to put value in lower 16 bits
  lw t5, 0(t0) # [t5]31:16 = switch values
  srli t5, t5, 16 # [t5]15:0 = switch values
figure of board from https://reference.digilentinc.com/

## Slide 74: RVfpga Lab 6: GPIO Low-Level Implementation
Divided in 3 main parts
  RVfpgaNexys’s external connection to the on-board LEDs/Switches (left shaded region)
  Integration of the GPIO module into SweRVolfX (middle shaded region)
  Connection between the GPIO and the SweRV EH1 (right shaded region)

## Slide 75: RVfpga Lab 6: External connection
File rvfpganexys.xdc: Defines the connection of i_sw[15:0] with the on-board switches and o_led[15:0] with the on-board LEDs

## Slide 76: RVfpga Lab 6: Integration into RVfpga
File swervolf_core.v: Tri-state buffers and GPIO module instantiation

## Slide 77: RVfpga Lab 6: Connection with SweRV EH1
File wb_intercon.v: 7-1 Multiplexer implementation

## Slide 78: Lab 7: 7-Segment Displays

## Slide 79: RVfpga Lab 7: 7-Segment Displays
Overview of 7-segment displays
7-segment display hardware

## Slide 80: RVfpga Lab 7: Overview of 7-Segment Displays
A
B
C
F
E
G
D
7 LED segments: A-G
Light up segments to create specific digit
  1: segments B and C
  2: segments A, B, D, E, G
  3: segments A, B, C, D, G
  etc.

## Slide 81: RVfpga Lab 7: 7-Segment Displays on Nexys A7
figure of board from https://reference.digilentinc.com/
8-digit 7-segment displays
Memory-mapped access:
  Enables_Reg: 0x80001038
  Digits_Reg: 0x8000103C
Enables are low-asserted
Example: Display 71 on two right-most digits:
  Enables_Reg = 0xFC (0b11111100: enable two right-most digits)
  Digits_Reg = 0x71
  Assembly: li t0, 0x80001038
  li t1, 0xFC
  li t2, 0x71
  sw t1, 0(t0)
  sw t2, 4(t0)

## Slide 82: RVfpga Lab 7: 7-Segment Display Hardware
8-Digit 7-Segment Displays
Each digit is common anode (anodes of that digit’s LEDs are tied together)
  Anode signals act as enables (AN0 - AN7)
  Drive low to enable digit (AN0 - AN7 go through an inverter (not shown) before being fed to LED)
Each segment for all digits is tied together
  Segments are driven low to turn them on
  Time-multiplexing of AN0 - AN7 signals allows unique values to be displayed on each digit
  A digit’s AN signal (AN0 - AN7) must go low every 1-16 ms to be bright

## Slide 83: RVfpga Lab 7: 7-Seg. Disp. Low-Level Implementation
Divided in 3 main parts
  RvfpgaNexys’s external connection to the on-board 7-seg. displays (left shaded region)
  Integration of the 7-seg. displays module into SweRVolfX (middle shaded region)
  Connection between the 7-seg. disp. and the SweRV EH1 (right shaded region)

## Slide 84: RVfpga Lab 7: External connection
File rvfpganexys.xdc: Defines the connection of CA-CG (called Digits_Bits[i] in the SoC) and AN[i] with the on-board 7-segment displays

## Slide 85: RVfpga Lab 7: Integration into SweRVolfX
File swervolf_syscon.v: 7-segment displays controller instantiation. The module receives, in addition to the clock signal (i_clk) and the reset signal (i_rst), two input signals, Enables_Reg and Digits_Reg, which are the two memory-mapped control registers described before. This module outputs two signals, AN and Digits_Bits, which are connected to the 7-segment displays on the board.

## Slide 86: RVfpga Lab 7: Integration into SweRVolfX
The SevSegDisplays_Controller is also implemented in this file. It contains the following subunits:
  Two multiplexers (module SevSegMux) that select the value to send to the AN and Digits_Bits signals every 2ms.
  A counter (module counter) that creates the 2ms period.
  A decoder (module SevenSegDecoder), which outputs the segment values for a given 4-bit hexadecimal value.

## Slide 87: Lab 8: Timers

## Slide 88: RVfpga Lab 8: Timers
Overview of timers
Timer Registers
Timer Example

## Slide 89: RVfpga Lab 8: Timers
Timers increment or decrement a counter at a fixed frequency
Commonly found in microcontrollers and SoCs
Used to generate precise timing

## Slide 90: RVfpga Lab 8: Timers
The Timer module used is from OpenCores: https://opencores.org/projects/ptc
Peripherals

## Slide 91: RVfpga Lab 8: Timer (PTC) Module
Timer module (also called the PTC module) is used for:
  Timer/Counter: counts clock edges (or edges of another signal, also called events)
  Pulse-width modulation (PWM):
    Vary high duration (called duty cycle) of an output
    Used to approximate an analog voltage digitally
PWM example: 33% duty cycle (signal is high 1/3rd of the time). If high level is 3 V, analog voltage (average voltage of signal) is 3 V * 0.33 = 1 V

## Slide 92: RVfpga Lab 8: Timer (PTC) Registers
Name | Address | Width | Access | Description
RPTC_CNTR | 0x80001200 | 1-32 | R/W | Main PTC counter
RPTC_HRC | 0x80001204 | 1-32 | R/W | PTC HI Reference/Capture register
RPTC_LRC | 0x80001208 | 1-32 | R/W | PTC LO Reference/Capture register
RPTC_CTRL | 0x8000120C | 9 | R/W | Control register
RPTC_CNTR: Counter (value of the counter)
RPTC_HRC: High reference capture – indicates the number of cycles (after reset) when the output should go high in PWM mode
RPTC_LRC: Low reference capture – indicates the number of cycles (after reset) when the count is complete in counter/timer mode; indicates the number of clock cycles (after reset) when the output should go low in PWM mode.
RPTC_CTRL: Control register

## Slide 93: RVfpga Lab 8: Timer (PTC) Control Register
Bit | Access | Reset | Name & Description
0 | R/W | 0 | EN: When set, RPTC_CNTR increments.
1 | R/W | 0 | ECLK: Selects the clock signal: external clock, through ptc_ecgt (1), or system clock (0).
2 | R/W | 0 | NEC: Used for selecting the negative/positive edge and low/high period of the external clock (ptc_ecgt).
3 | R/W | 0 | OE: Enables PWM output driver.
4 | R/W | 0 | SINGLE: When set, RPTC_CNTR is not incremented after it reaches value equal to the RPTC_LRC value. When cleared, RPTC_CNTR is restarted after it reaches value in the RPTC_LCR register.
5 | R/W | 0 | INTE: When set, PTC asserts an interrupt when RPTC_CNTR value is equal to the value of RPTC_LRC or RPTC_HRC. When the signal is cleared, interrupts are masked.
6 | R/W | 0 | INT: When read, this bit represents pending interrupt. When it is set, an interrupt is pending. When this bit is written with ‘1’, interrupt request is cleared.
7 | R/W | 0 | CNTRRST: When set, RPTC_CNTR is reset. When cleared, normal operation of the counter occurs.
8 | R/W | 0 | CAPTE: When set, RPTC_CNTR is captured into RPTC_LRC or RPTC_HRC registers. When cleared, capture function is masked.

## Slide 94: RVfpga Lab 8: Timer Example
Set RPTC_LRC to number of cycles to count
Set control bits (RPTC_CTRL) to configure timer:
  Reset counter and clear interrupts: RPTC_CTRL = 0xC0 (0b011000000): CNTRRST (bit 7) = 1: counter is reset (RPTC_CNTR = 0); INT (bit 6) = 1: interrupt request cleared.
  Enable counter and interrupts: RPTC_CTRL = 0x21 (0b000100001): EN (bit 0) = 1: counter is enabled, so RPTC_CNTR increments; INTE (bit 5) = 1: PTC asserts an interrupt when RPTC_CNTR == RPTC_LRC.
Program reads interrupt bit in control register (INT is bit 6 of RPTC_CTRL) until it is 1 (indicating that RPTC_CNTR == RPTC_LRC).
This algorithm does not use interrupts, but it does read the interrupt bit (INT, bit 6 of RPTC_CTRL) to determine when the correct number of clock cycles have been reached. We show how to use interrupts in Lab 9.

## Slide 95: RVfpga Lab 8: Timer Low-Level Implementation
Divided in 2 main parts
  (No external connection)
  Integration of the Timer module into SweRVolfX (left shaded region)
  Connection between the Timer and the SweRV EH1 (right shaded region)

## Slide 96: RVfpga Lab 8: Integration into SweRVolfX
File swervolf_core.v: PTC module instantiation

## Slide 97: Lab 9: Interrupt-Driven I/O

## Slide 98: RVfpga Lab 9: Interrupt-Driven I/O
Interrupt-driven I/O vs. Programmed I/O
Rvfpga System’s Interrupt Controller
How to configure interrupts using Western Digital’s Peripherals Support and Board Support Packages (PSP and BSP)
Interrupt Example

## Slide 99: RVfpga Lab 9: Interrupt-Driven I/O Introduction
Programmed I/O:
  A program continuously polls a value (for example a switch) until the desired value is seen.
  For example, this method was used to read the switches in prior labs.
  This ties up the processor by its constantly polling a value – instead of being able to do other useful work.
Interrupt-driven I/O:
  An event (such as a pin asserting) causes the processor to jump to an interrupt service routine (ISR, also called an interrupt handler), which is like an unscheduled function call. The ISR handles the interrupt – for example, reads the value of the switches – and then returns to the regular program.
  Until that event occurs, the processor can continue doing useful work.

## Slide 100: RVfpga Lab 9: Handling Interrupts
Interrupts may be caused by hardware or software
In this lab, we focus on hardware interrupts
The SweRV EH1 core handles interrupts after RISC-V’s PLIC (Platform-level interrupt controller) specification. It is referred to as the Programmable Interrupt Controller (PIC). It has:
  255 interrupt sources
  15 priority levels

## Slide 101: RVfpga Lab 9: Interrupt Hardware

## Slide 102: RVfpga Lab 9: Single-vector vs. Multi-vector mode
Single-vector mode example:
Multi-vector mode example:

## Slide 103: RVfpga Lab 9: Handling Interrupts
Using WD’s PSP/BSP:
  Initialize Interrupts using WD’S PSP/BSP
  Initialize one or more of the 255 interrupts and provide name of ISR
  Connect peripheral signal that should trigger interrupt with interrupt pin.
  Enable all interrupts
  Enable external interrupts

## Slide 104: RVfpga Lab 9: Interrupt Example
Use interrupts to read value of Switch[0] – only on rising edge (01 transition)
Name | Address | Width | Access | Description
RGPIO_IN | 0x80001400 | 1-32 | R | GPIO input data
RGPIO_OUT | 0x80001404 | 1-32 | R/W | GPIO output data
RGPIO_OE | 0x80001408 | 1-32 | R/W | GPIO output driver enable
RGPIO_INTE | 0x8000140C | 1-32 | R/W | Interrupt enable
RGPIO_PTRIG | 0x80001410 | 1-32 | R/W | Type of event that triggers an interrupt
RGPIO_AUX | 0x80001414 | 1-32 | R/W | Multiplex auxiliary inputs to GPIO outputs
RGPIO_CTRL | 0x80001418 | 2 | R/W | Control register
RGPIO_INTS | 0x8000141C | 1-32 | R/W | Interrupt status
RGPIO_ECLK | 0x80001420 | 1-32 | R/W | Enable gpio_eclk to latch RGPIO_IN
RGPIO_NEC | 0x80001424 | 1-32 | R/W | Select active edge of gpio_eclk
For full code, see: [RVfpgaPath]/RVfpga/Labs/Lab9/LED-Switch_7SegDispl_Interrupts_C-Lang.c

## Slide 105: RVfpga Lab 9: Interrupt Example
Setting up GPIO registers for interrupts:
  RGPIO_INTE = 0x10000 (enable interrupt for Switch[0])
  RGPIO_PTRIG = 0x10000 (interrupt triggered on rising-edge of Switch[0])
  RGPIO_INTS = 0x0 (clears all interrupts)
  RGPIO_CTRL = 0x1 (enables GPIO interrupts)

## Slide 106: RVfpga Lab 9: Interrupt Example
GPIO ISR:
void GPIO_ISR(void) {
unsigned int i;
/* Invert LED value */
i = M_PSP_READ_REGISTER_32(GPIO_LEDs); /* RGPIO_OUT */
i = !i; /* Invert the LEDs */
i = i & 0x1; /* Only keep right-most LED */
M_PSP_WRITE_REGISTER_32(GPIO_LEDs, i) /* RGPIO_OUT */
/* Clear GPIO interrupt */
M_PSP_WRITE_REGISTER_32(RGPIO_INTS, 0x0); /* RGPIO_INTS */
/* Stop the generation of this interrupt (IRQ4) */
bspClearExtInterrupt(4);
}

## Slide 107: RVfpga Lab 9: Interrupt Example
Connect interrupt 4 (IRQ4) with interrupt from switch, and set interrupt service routine to be GPIO_ISR
Memory-mapped register 0x80001018 = 0x1: connects GPIO interrupt to IRQ4
Enable global interrupts

## Slide 108: Lab 10: Serial Buses

## Slide 109: RVfpga Lab 10: Serial Buses
Serial buses send one bit at a time
  In contrast, parallel buses send multiple bits at once
Common serial buses
  UART (universal asynchronous receiver/transmitter)
  SPI (serial peripheral interface)
  I2C (inter-integrated circuit protocol)
We focus on SPI in this lab

## Slide 110: RVfpga Lab 10: Serial Buses
Controller: sends clock, sends & receives data
Peripheral: receives clock, sends & receives data
Signals:
  SDO: Serial Data Out
  SDI: Serial Data In
  SCK: SPI clock
  CSbar: low-asserted chip select

## Slide 111: RVfpga Lab 10: Serial Buses
SCK idles
When controller sends edge on SCK, both controller and peripheral sample and send data. Data is changed (sent) on falling edge and sampled on rising edge (although this is configurable)

## Slide 112: RVfpga Lab 10: Rvfpga System’s SPI Module
Rvfpga System’s SPI module is from OpenCores
https://opencores.org/projects/simple_spi
4-entry read and write buffers
SPI Registers:
Name | Address | Width | Access | Description
SPCR | 0x80001100 | 8 | R/W | Control register
SPSR | 0x80001108 | 8 | R/W | Status register
SPDR | 0x80001110 | 8 | R/W | Data register
SPER | 0x80001118 | 8 | R/W | Extensions register
SPCS | 0x80001120 | 8 | R/W | CS register

## Slide 113: RVfpga Lab 10: ADXL362 Accelerometer
The Nexys A7 board includes an Analog Devices ADXL362 accelerometer. You can find the complete information at:
  https://www.analog.com/media/en/technical-documentation/data-sheets/ADXL362.pdf

## Slide 114: RVfpga Lab 10: Accel. Low-Level Implementation
Divided in 3 main parts
  RvfpgaNexys external connection to the on-board accelerometer (left shaded region)
  Integration of the new SPI module into SweRVolfX (middle shaded region)
  Connection between the accelerometer and the SweRV EH1 (right shaded region)

## Slide 115: RVfpga Lab 10: External connection
File rvfpganexys.xdc: Defines the connection of the SPI signals used in the SoC with the corresponding on-board accelerometer pins

## Slide 116: RVfpga Lab 10: Integration into SweRVolfX
File swervolf_core.v: Tri-state buffers and GPIO module instantiation